## Slide 1: AM Questions

## Slide 2
Topology
OSI model
TCP/IP model

## Slide 3: When a network device is connected to the LAN with the network address of 201.12.1.64 and the subnet mask of 255.255.255.192, which of the following IP addresses should NOT be assigned to the device on the network ?
A. 201.12.1.65
B. 201.12.1.96
C. 201.12.1.126
D. 201.12.1.127
Notes: Lesson descriptions should be brief.

## Slide 4: Which of the following is the appropriate protocol that is widely used with TCP/IP networks to collect and manage information from network devices such as servers, routers, switches, and hubs ?
A. HTTP
B. HTTPS
C. SMTP
D. SNMP
Notes: Lesson descriptions should be brief.

## Slide 5: Which of the following occurs when computer A broadcasts an ARP request to find the MAC address of computer B on the same network ?
A. All computers in network receive the request from A, and all of them reply to A with the MAC address of B.
B. All computers in network receive the request from A, and only B replies to A with its MAC address.
C. DNS server replies to A with the MAC address of B
D. The nearest router that receives the request from A replies to A with the MAC address of B or forwards the request to another router.
Notes: Lesson descriptions should be brief.

## Slide 6: Which of the following provides the function of mapping between domain names and IP addresses in a TCP/IP network ?
A. DHCP
B. DNS
C. SNMP
D. Proxy
Notes: Lesson descriptions should be brief.

## Slide 7: Which of the following layers of an OSI basic reference model is comparable to an HDLC procedure ?
A. Data link layer
B. Transport Layer
C. Network Layer
D. Physical Layer
Notes: Lesson descriptions should be brief.

## Slide 8: Which of the following is a connectionless protocol that offers speed and low overhead as its primary advantage in the transport layer of the OSI basic reference model?
A. ARP
B. ICMP
C. IP
D. UDP
Notes: Lesson descriptions should be brief.

## Slide 9: What protocol dynamically assigns IP addresses in a TCP/IP network ?
A. ARP
B. DHCP
C. RIP
D. SMTP
Notes: Lesson descriptions should be brief.

## Slide 10: In a CSMA/CD LAN, which of the following is used in the data link layer to identify the sender and destination when sending and receiving frames ?
A. Host ID in an IP address
B. MAC Address
C. Subnet mask
D. Port No
Notes: Lesson descriptions should be brief.

## Slide 11: In the OSI 7-layer model, which of the following layers converts data from the upper layer into many tiny pieces called segments for transmission across the network ?
A. Data link layer
B. Network layer
C. Physical layer
D. Transport Layer
Notes: Lesson descriptions should be brief.

## Slide 12: Among the layers of the OSI basic reference model, which of the following is the appropriate layer that is primarily responsible for the translation, encryption, and compression of data?
A. Data link layer
B. Physical layer
C. Presentation layer
D. Session layer

## Slide 13: Which of the following protocols is used in a TCP/IP network to provide a virtual terminal function that enables remote login to a host for remote operation ?
A. FTP
B. HTTP
C. SMTP
D. TELNET
Notes: Lesson descriptions should be brief.

## Slide 14: Which of the following is the IP address range that is reserved for class B in traditional IPv4 addresses?
A. 127.0.0.1 through 127.255.255.255
B. 128.0.0.0 through 191.255.255.255
C. 172.16.0.1 through 173.31.255.255
D. 192.168.0.1 through 192.168.255.255

## Slide 15: In the OSI basic conference model, which of the following layers provides a set of rules for establishing and terminating the connection between applications on computer systems ?
A. Datalink layer
B. Network layer
C. Session layer
D. Transport layer
Notes: Lesson descriptions should be brief.

## Slide 16: Which of the following protocols is used on the transport layer of OSI basic reference model ?
A. FTP
B. PPP
C. SNMP
D. UDP
Notes: Lesson descriptions should be brief.

## Slide 17: Which of the following IP addresses can be used to connect a computer direcly to the Internet ?
A. 10.10.11.88
B. 127.0.0.1
C. 172.16.255.255
D. 203.162.1.160
Notes: Lesson descriptions should be brief.

## Slide 18: In the OSI basic reference model, which of the following is the appropriate layer that provides end-to-end communication services for applications, and also provides convenient services such as connection-oriented or connectionless data stream support, reliability, flow control, and congestion control?
A. Data link layer
B. Network layer
C. Session layer
D. Transport layer
Notes: Lesson descriptions should be brief.

## Slide 19: Which of the following network topologies is commonly used, especially in Fast or Gigabit Ethernet, for connecting network devices via a centralized unit such as a hub or a switch?
A. Bus
B. Mesh
C. Ring
D. Star
Notes: Lesson descriptions should be brief.

## Slide 20: Which of the following is a protocol used by the ping command in order to verify that the communication link between source and destination is working in the TCP/IP network environment?
A. ARP
B. ICMP
C. SMTP
D. SNMP
Notes: Lesson descriptions should be brief.

## Slide 21: Which of the following is the appropriate combination that is defined as a socket address in TCP/IP network environements?
A. IP address and port number
B. IP address and socket number
C. MAC address and port number
D. MAC address and socket number

## Slide 22: Which of the following is the broadcast MAC address that is used by multiple protocols, such as ARP (Address Resolution Protocol) and RIP (Routing Information Protocol), in order to transmit data to all of the hosts on the local subnet?
A. 00-00-00-00-00-00
B. F0-F0-F0-F0-F0-F0
C. EE-FF-EE-FF-EE-FF
D. FF-FF-FF-FF-FF-FF
Notes: Lesson descriptions should be brief.

## Slide 23: In an IPv4 environment, when the subnet mask “255.255.255.224” is used for a class C network, how many IP addresses including reserved or ineffective addresses can be assigned to subnets and hosts per subnet respectively?
A. Subnet:8 and Host:32
B. Subnet:16 and Host:16
C. Subnet:16 and Host:32
D. Subnet:32 and Host:8
Notes: Lesson descriptions should be brief.

## Slide 24
LAN
WAN
Services on Internet

## Slide 25: Which of the following terms can be applicable to an explanation below ? "The sender sends a single datagram; the routers are responsible for making copies and sending them to a group of interested receivers"
A. Anycast
B. Broadcast
C. Multicast
D. Unicast
Notes: Lesson descriptions should be brief.

## Slide 26: Which of the following is an appropriate function of a switching hub (layer 2 switch) that is used as a network device?
A. A received packet is divided (i.e., fragmented into multiple in the network layer
B. A received packet is forwarded (i.e., broadcasted) to all LAN ports
C. A received packet is forwarded only to a LAN port corresponding to a destination MAC address
D. An IP address for a terminal connected to a LAN port is dynamically allocated.
Notes: Lesson descriptions should be brief.

## Slide 27: Which of the following protocols is used for synchronizing the clocks in multiple nodes on the Internet ?
A. NNTP
B. NTP
C. SMTP
D. SNMP
Notes: Lesson descriptions should be brief.

## Slide 28: Which of the following protocols can be used to access e-mail messages that are stored on a remote, and possibly shared, mail server, and there by are manipulated from a desktop computer at home, a workstation at the office, and a notebook computer while traveling, without the need to transfer messages back and forth between these computers?
A. FTP
B. IMAP
C. POP3
D. SMTP
Notes: Lesson descriptions should be brief.

## Slide 29: The function that starts up a computer via a LAN is called WOL (Wake on LAN). Which of the following can be performed efficiently by using this function?
A. Detection of a system malfunction
B. Maintenance of a PC at a remote location
C. Management of the traffic condition
D. Monitoring of unauthorized access
Notes: Lesson descriptions should be brief.

## Slide 30: Which of the following describes the role of DNS in the TCP/IP network?
A. Allocating an unused IP address from the IP addresses registered in the server, in response to a request from a PC for IP address assignment
B. Enabling access to the Internet by converting an in-company private IP address into a global IP address
C. Linking a name, such as a domain name or a host name, with an IP address
D. Making it possible to call a program in a server by specifying its name without regard to the IP address of the server
Notes: Lesson descriptions should be brief.

## Slide 31: Which of the following is an appropriate combination of the protocols that are used for transmitting and receiving e-mail as shown in the diagram below?
A. POP3(1) POP3(2) SMTP(3)
B. POP3(1) SMTP(2) POP3(3)
C. SMTP(1) POP3(2) SMTP(3)
D. SMTP(1) SMTP(2) SMTP(3)
Notes: Lesson descriptions should be brief.

## Slide 32: Which of the following is the appropriate technology that is used to establish a private or secure network connection within a public IP network. such as the Internet, and to give the company the same capabilities at much lower cost by using the shared public infrastructure rather than a private one ?
A. Firewall
B. Pat
C. RPC
D. VPN
Notes: Lesson descriptions should be brief.

## Slide 33: Which of the following is an appropriate statement in regard to the transmission operation of nodes connected to a LAN in the CSMA/CD Method ?
A. Each node checks whether the carrier is busy and can transmit only if the carrier is not busy. When collision is detected, transmission is tried again after a random time has eslapsed.
B. Each node checks whether the carrier is busy and can transmit only if the carrier is not busy. When collision is detected, transmission is tried again after a random time has eslapsed.
C. Only the node that has been assigned a time slot can transmit
D. The nodes are connected in a ring, a special frame for controlling transmission privileges is circulated, and only the node that has received this frame can transmit.
Notes: Lesson descriptions should be brief.

## Slide 34: Which of the following is the key technology that enables to connect a computer using a private IP address to the Internet ?
A. BOOTP
B. DHCP
C. NAT
D. RARP
Notes: Lesson descriptions should be brief.

## Slide 35: Which of the following is the appropriate protocol that is used to send e-mail messages from one server to another over the Internet ?
A. FTP
B. HTTP
C. POP3
D. SMTP
Notes: Lesson descriptions should be brief.

## Slide 36: Which of the following is an mechanism that allows a Web server to store its own information about a user on the user's own computer so that the Web server can identify users and possibly prepare customized Web pages for them ?
A. Cookie
B. Password
C. SSL
D. URL
Notes: Lesson descriptions should be brief.

## Slide 37: Which of the following is the server that can be used to intercept all messages entering and leaving the network and to effectively hide the true network addresses?
A. DHCP Server
B. DNS Server
C. E-mail Server
D. Proxy Server
Notes: Lesson descriptions should be brief.

## Slide 38: Which of the following is used for encoding and interpreting binary files, images, video, and not-ASCII character sets within an e-mail message on the Internet?
A. IMAP
B. MIME
C. POP3
D. SMTP
Notes: Lesson descriptions should be brief.

## Slide 39
Network Security

## Slide 40: Which of the following is the public key cryptography algorithm that is named after the initials its three researchers and is based on the difficulty of factorizing extremely large numbers into prime factors?
A.AES
B. DES
C. DSA
D. RSA

## Slide 41: Which of the following explains the pattern matching method that is used by antivirus software?
A. Viruses are detected by comparing files before infection with files after infection to investigate whether any change has been made to the files.
B. Viruses are detected by comparison with the file checksum.
C. Viruses are detected by comparison with the signature codes of known viruses.
D. Viruses are detected by monitoring the system for abnormal phenomena caused by viruses.
Notes: Lesson descriptions should be brief.

## Slide 42: A government website accepts passport applications using HTTP forms to collect information. Users provide complete personal information in the forms to help expedite processing of face-to-face transactions, and payments are done offline. The information collected enters a secure server for processing and document releasing. In this system environment, which of the following is the most likely security attack?
A. Password-guessing attack
B. Sniffing traffic for identity theft
C. Spamming to attain denial of service
D. Spoofing attack
Notes: Lesson descriptions should be brief.

## Slide 43: Which of the following is a network segment that is isolated from the external network (WAN) and the internal network (LAN) via firewalls in order to ensure that publicly accessible servers cannot contact other internal network segments in the event that such a server is compromised?
A. DMZ
B. DNS
C. Proxy
D. VLAN
Notes: Lesson descriptions should be brief.

## Slide 44: When information, such as an e-mail or a document file, is sent or received with a digital signature via the Internet, which of the following is the appropriate combination of security properties that ensure that such information has not been altered or tampered with during transmission?
A. Atomicity and consistency
B. Authenticity and integrity
C. Availability and confidentiality
D. Durability and isolation
Notes: Lesson descriptions should be brief.

## Slide 45: When a message is sent to Person A from Person B using public key cryptography, which of the following keys should be used for encrypting the message?
A. A’s private key
B. A’s public key
C. B’s private key
D. B’s public key
Notes: Lesson descriptions should be brief.

## Slide 46: Which of the following refers to online scams where thieves attempt to entice e-mail recipients into clicking on a link that takes them to a bogus website, and the website may prompt the recipient to provide personal information such as social security number, bank account number, and credit card number, and/or it may download malicious software onto the recipient’s computer?
A. Cross site scripting
B. DoS attack
C. Phishing
D. Trojan horse
Notes: Lesson descriptions should be brief.

## Slide 47: A message with a digital signature is received via e-mail. Which of the following can be checked by verifying the digital signature of the received message?
A. The email has not been leaked
B. The email has not been relayed improperly
C. The message has not been falsified
D. The message has not been retransmitted on specific data and time
Notes: Lesson descriptions should be brief.

## Slide 48: Which of the following is a technique of social engineering that obtains sensitive or confidential data by searching for residual data left in a computer after job execution or by examining discarded or stolen media such as printed papers, tapes, and discs?
A. Salami technique
B. Scavenging
C. Sniffing
D. Spoofing

## Slide 49: Which of the following is a biometric recognition technique that is used for identifying a person by using the person’s own behavioral features as well as physiological features?
A. Fingerprint recognition
B. Iris recognition
C. Vein recognition
D. Voice recognition

## Slide 50: In e-commerce such as mail-order business, there is a risk that dealers or users are damaged by falsifying, spoofing, and repudiation at the time of sales order or purchase order. Which of the following is an appropriate security technology that can cope well with all of these three threats?
A. Digital signature
B. Firewall
C. Junk mail filter
D. Virus check

## Slide 51: Which of the following is an algorithm that can be used for asymmetric (or public key) cryptography?
A. AES
B. DES
C. RC4
D. RSA
Notes: Lesson descriptions should be brief.

## Slide 52: Which of the following is the purpose of using a WAF (Web application firewall)?
A. To block attacks to a vulnerability arising from a web server and an application
B. To detect the intrusion of a worm in a web server and remove the worm automatically
C. To detect vulnerabilities and inconsistencies of applications in an integration test during content development for a web server
D. To find security holes of a web server and apply OS security patches

## Slide 53: Port scanning is the process of sending packets to check every port on each target system to see which ports are open and which ports are locked. Which of the following information can be identified by port scanning?
A. Computer viruses in activity
B. Hardware configuration and compatibility
C. Network and application services currently available
D. Operating system in execution
Notes: Lesson descriptions should be brief.

## Slide 54: Which of the following can be realized by using the packet filtering function of a firewall?
A. To allow only the packets with specific TCP port numbers to pass from the Internet through to the internal network
B. To change a packet with a dynamically assigned TCP port number to a TCP port number that is fixed at the receiving side and allow it to pass through to the internal network
C. To check for tampering in the header and/ or data of a packet received on the Internet and remove the packet if tampering has been found
D. To repair a packet received on the Internet if it has been tampered with, or to record the packet in a log and prevent the packet from passing through to the internal network if the tampering cannot be repaired
Notes: Lesson descriptions should be brief.

## Slide 55: Which of the following is an appropriate purpose of installing a firewall in a computer network?
A. To authenticate internal users
B. To block and permit data traffic
C. To protect a computer from computer viruses
D. To verify company policies
Notes: Lesson descriptions should be brief.

## Slide 56: Against what kind of attacks does SSL (Secure Socket Layer) protect users on the Internet ?
A. Bruce force attack
B. Dos (Denial Of Service) attack
C. IP spoofing
D. Tapping and exploitation of data
Notes: Lesson descriptions should be brief.

## Slide 57: Which of the following is a method of phising ?
A. A virus-infected computer is controlled from the outside via a network such as the Internet
B. Personal information such as the IP address and Web browsing history of computer users is secretly collected and sent to the outside.
C. Someone sends e-mails to entice the recipients and to have them access fake Web sites that appear to be sites of actually existing companies etc. and steals personal information
D. When there is a part that directly displays what has been entered on a Web page, a malicious script is embedded within the page, causing damage to the user and the server.
Notes: Lesson descriptions should be brief.

## Slide 58: Which of the following is the salami technique used in computer crime ?
A. Illegally intercepting audio and/or data being transmitted or received on a network
B. Secretly gaining access to a part of the line to steal someone's password and/or ID and to steal data
C. Secretly searching for information left inside or around a computer after a program is executed, for the purpose of obtaining necessary information
D. Stealing from multiple assets little by little, to a degree that the illegal action does not come to the surface and become noticeable
Notes: Lesson descriptions should be brief.

## Slide 59: Which of the following is an appropriate action to be taken when a computer virus is found ?
A. First, the computer is powered off, because the virus program may be resident in memory.
B. First, the infected computer is disconnected from the relevant network, because other computers may be infected via the network
C. If a worm that infects a wide area in a short period of time is found while an online business system is running, the virus countermeasure is taken without stopping the system.
D. The reproducibility of virus activities is confirmed for the purpose of identifying the virus name by special characteristics activated at the time of infection.
Notes: Lesson descriptions should be brief.

## Slide 60: Which of the following is an advantageous effect of encrypting e-mails ?
A. It is possible to prevent denial-of-service attacks against e-mails
B. It is possible to prevent encryption keys from being lost.
C. It is possible to prevent the contents of e-mails from leaking out
D. It is possible to protect transmission records on mail servers from being falsified.
Notes: Lesson descriptions should be brief.

## Slide 61: Which of the following is an appropriate description concerning social engineering?
A. An attacker creates IP packets that appear to originate from valid addresses inside a trusted network
B. An attacker intercepts and modifies the data in the packet without the knowledge of the sender or receiver
C. An attacker manipulates people into providing inappropriate access to sensitive or confidential data
D. An attacker searches for a valid combination of user ID and password by using a brute force attack tool
Notes: Lesson descriptions should be brief.

## Slide 62: Which of the following is a collection of infected computers that have been compromised without their owners realizing it and are being remotely controlled by attackers, in order to typically send spam or attack other computers
A. Botnet
B. Honeynet
C. Rootkit
D. Web beacon

## Slide 63: Which of the following is a method that is used to check if an image or other digital content has been illegally copied and resold?
A. Digital certificate
B. Digital preservation
C. Digital signature
D. Digital watermark
Notes: Lesson descriptions should be brief.