## Slide 1: Network overview

## Slide 2: Introduction
Exploring the functions of networking
Topology
OSI model
TCP/IP model

## Slide 3: What is a network?
A collection of devices and end systems that can communicate with each other
Environments
  Homes
  Small businesses
  Large enterprises
Notes: Lesson descriptions should be brief.

## Slide 4: Large enterprise network
Main office
  Several buildings
  Hundreds of employee
Remote location
  Branch office:
    Local network resource
    Access information from main office
  Home office
    on-demand connections to the main or branch offices
  Mobile users
    Connect while traveling

## Slide 5: Network Classification

## Slide 6: Characteristics of a Network
Speed (data rate):
  How fast data is transmitted
Cost
  Cost of components, installation, and maintenance
Security
  Both storage data and transmitted data
Availability
  24/7
Scalability
  Meet new needs when the network grows.
Reliability
  Probability of failure
Topology

## Slide 7: What is a Topology
The way in which the connections are made among all the computers is called the topology of the network.
Network topology specifically refers to the physical layout of the network, specially the location of the computers and how the cable is run between them.
The most common topologies are:
  Bus
  Star
  Ring Mesh
Notes: Việc kết nối các máy tính và các thiết bị đầu cuối,v.v.. qua đường truyền tạo nên khả năng xây dựng nhiều loại cấu hình mạng khác nhau, tương ứng với quy mô và mục đích sử dụng.

## Slide 8: Bus Topology
The bus topology is the best simplest and most common
It is often used when a network installation is small, simple, or temporary
On a bus network, all the computer are connected to a single cable
Failure of one node does not affect the rest of network
Notes: • Đây là kiểu đi dây đơn giản nhất nhưng nếu một đầu cuối bị bỏ đi thì việc đi dây bus cần phải
làm lại.
• Có một số hạn chế về độ dài của bus và số lượng đầucuối có thể kết nối .
• Dữ liệu được gửi từ đầu cuối đi theo luồn tới tất cả các đầu cuối khác cho phép việc truyền tới
nhiều đích (quảng bá- broadcasting).
• Đầu cuối sẽ nắm bắt dữ liệu nhận được nếu như địa chỉ đích gửi trùng với địa chỉ đầu cuối.
• Các dữ liệu không cần thiết có thể còn lại trên đường liên lạc, nhưng dữ liệu đó có thể bị loại bỏ
bởi các "thiết bị cuối" nối hai đầu của cáp truyền.
• Sự xung đột có thể xảy ra nếu dữ liệu từ nhiều đầu cuối được gửi đồng bộ.

## Slide 9: Star Topology
In a star topology, each device has a dedicated point to point link only to central controller usually called a hub/server/host/
It is easy to modify and add new computers to a star network
Single computer failure do not necessarily bring down the whole star network
If the central hub fails, the whole network fails to operate
Notes: Trong kiểu sao, nhiều đầu cuối được kết nối vào mộtbộ tập trung (hub hoặc PBX, ...) trong một cấu
hình được bố trí theo hình sao
Tính năng của mạng sao là:
• Dễ thêm và bớt các đầu cuối được kết nối vào mạng.
• Phụ thuộc và khả năng của bộ tập trung, có những hạn chế về số lượng đầu cuối có thể kết nối và
khoảng cách truyền từ bộ tập trung.
• Thậm chí nếu một đầu cuối hỏng cũng không ảnh hưởngđến hệ thống tổng thể, nhưng nếu bộ tập
trung hỏng, thì toàn bộ mạng sẽ sập vì dữ liệu đượctrao đổi bằng cách đi qua bộ tập trung

## Slide 10: Ring Topology
In a ring topology, each computer is connected directly to the next computer in line, forming a circle of cable.
It uses token to pass the information from one computer to another.
Failure of one computer can affect the whole network
Notes: • Dữ liệu được gửi từ đầu cuối sẽ đi quanh vòng theo một chiều.
• Đầu cuối nắm bắt dữ liệu nhận được nếu như địa chỉ đích gửi trùng với địa chỉ đầu cuối. Nếu
không phải, nó chuyển dữ liệu đến đầu cuối tiếp theo.
• Điều khiển truyền dữ liệu (truyền thẻ bài- token passing) có thể được dùng để xác định xem đầu
cuối nào được phép truyền dữ liệu để tránh xung độtxảy ra do việc truyền dữ liệu đồng thời từ
hai hoặc nhiều đầu cuối.
• Việc thiết lập các đường bỏ qua là cần thiết vì toàn bộ mạng sẽ ngừng hoạt động nếu chỉ một đầu
cuối bị hỏng.

## Slide 11: Mesh Topology
In a mesh topology, every devices has a dedicated point to point link to every other device
Failure of one node computer not affect rest of the network

## Slide 12: OSI Introduction
Communication rules
  Compare with human language
    Medium
    Grammar
  Multi-vendor  one standard  OSI model

## Slide 13: OSI model overview
Application
(Upper)
Layers
Session
Presentation
Application

## Slide 14: OSI model overview
Data Flow
Layers
Transport Layer
Data Link
Network Layer
Physical
Application
(Upper)
Layers
Session
Presentation
Application

## Slide 15: Role of Application Layers
Telnet
FTP
DNS
HTTP
SMTP
POP3
NNTP
SNMP
DHCP
User Interface
EXAMPLES
Application
Notes: Tầng ứng dụng là tầng cao nhất liên quan đến các dịch vụ gắn liền với các ứng dụng của người dùng.
Các dịch vụ trên Internet được thực hiện bởi các giao thức của tầng này.
• DNS (Hệ thống đánh tên miền): Giao thức ánh xạ các tên miền với địa chỉ IP.
• HTTP (Giao thức chuyển giao siêu văn bản): Giao thức truyền tệp trong ngôn ngữ HTML.
• FTP (File Transfer Protocol): Giao thức truyền tệp.
• SMTP (Simple Mail Transfer Protocol): Giao thức truyền thư đơn giản.
• POP3 (Post Office Protocol Version 3): Giao thứcnhận thư từ mail servers.
• NNTP (Network News Transfer Protocol): Giao thức truyền tin trên mạng.
• TELNET (TELecommunication NETwork): Giao thức cho phép truy nhập vào thiết bị đầu
cuối từ xa.
• SNMP (Simple Network Management Protocol): Giao thức quản lý mạng đơn giản.
• DHCP (Dynamic Host Configuration Protocol): Giao thức thiết lập địa chỉ IP động.

## Slide 16: Role of Application Layers
Telnet
FTP
ASCII
EBCDIC
JPEG
User Interface
How data is presented
Special processing such as encryption
EXAMPLES
Presentation
Application

## Slide 17: Role of Application Layers
Telnet
FTP
ASCII
EBCDIC
JPEG
Keeping different applications’
data separate
User Interface
How data is presented
Special processing such as encryption
Operating System/
Application Access
Scheduling
EXAMPLES
Session
Presentation
Application

## Slide 18: Role of Application Layers
Keeping different applications’
data separate
User Interface
How data is presented
Special processing such as encryption
Telnet
FTP
ASCII
EBCDIC
JPEG
Operating System/
Application Access
Scheduling
Transport Layer
Data Link
Network Layer
Physical
EXAMPLES
Session
Presentation
Application

## Slide 19: Role of Data Flow Layers
EIA/TIA-232 V.35
EXAMPLES
Physical
Move bits between devices
Specifies voltage, wire speed and pin-out cables

## Slide 20: Role of Data Flow Layers
802.3 / 802.2
HDLC
EIA/TIA-232 V.35
EXAMPLES
Data Link
Physical
Combines bits into bytes and bytes into frames
Access to media using MAC address
Error detection not correction
Move bits between devices
Specifies voltage, wire speed and pin-out cables

## Slide 21: Role of Data Flow Layers
802.3 / 802.2
HDLC
EIA/TIA-232 V.35
IP
IPX
EXAMPLES
Network
Data Link
Physical
Combines bits into bytes and bytes into frames
Access to media using MAC address
Error detection not correction
Move bits between devices
Specifies voltage, wire speed and pin-out cables
Provide logical addressing which routers use for path determination

## Slide 22: Role of Data Flow Layers
TCP
UDP
SPX
802.3 / 802.2
HDLC
EIA/TIA-232 V.35
IP
IPX
EXAMPLES
Transport
Data Link
Physical
Reliable or unreliable delivery
Error correction before retransmit
Combines bits into bytes and bytes into frames
Access to media using MAC address
Error detection not correction
Move bits between devices
Specifies voltage, wire speed and pin-out cables
Network
Provide logical addressing which routers use for path determination

## Slide 23: Role of Data Flow Layers
TCP
UDP
SPX
802.3 / 802.2
HDLC
EIA/TIA-232 V.35
IP
IPX
Presentation
Application
Session
EXAMPLES
Reliable or unreliable delivery
Error correction before retransmit
Combines bits into bytes and bytes into frames
Access to media using MAC address
Error detection not correction
Move bits between devices
Specifies voltage, wire speed and pin-out cables
Transport
Data Link
Physical
Network
Provide logical addressing which routers use for path determination

## Slide 24: Encapsulating Data
Transport
Data Link
Physical
Network
Upper Layer Data
Upper Layer Data
TCP Header
Data
IP Header
Data
LLC Header
0101110101001000010
Data
MAC Header
Presentation
Application
Session
Segment
Packet
Bits
Frame
PDU
FCS
FCS

## Slide 25: De-encapsulating Data
Upper Layer Data
LLC Hdr + IP + TCP + Upper Layer Data
MAC Header
IP + TCP + Upper Layer Data
LLC Header
TCP+ Upper Layer Data
IP Header
Upper Layer Data
TCP Header
0101110101001000010
Transport
Data Link
Physical
Network
Presentation
Application
Session

## Slide 26: TCP/IP model
IP address overview
Transport layer
ARP
Exploring PC – PC communication
Notes: TCP/IP (Giao thức điều khiển truyền/Giao thức Internet - Transmission Control Protocol/Internet Protocol) đã trở thành giao thức chuẩn cho Internet. Do sự lan rộng của Internet,TCP/IP đã trở thành giao thức mạngchuẩn thực tế.

## Slide 27: IPv4 addressing
255
255
255
255
Dotted Decimal
Maximum
Network
Host
128 64 32 16 8 4 2 1
11111111
11111111
11111111
11111111
10101100
00010000
01111010
11001100
Binary
32 bits
172
16
122
204
Example Decimal
Example Binary
1
8
9
16
17
24
25
32
128 64 32 16 8 4 2 1
128 64 32 16 8 4 2 1
128 64 32 16 8 4 2 1

## Slide 28: IP address class
Class A:
Class B:
Class C:
Class D: Multicast
Class E: Research
Network
Host
Host
Host
Network
Network
Host
Host
Network
Network
Network
Host
8 bits
8 bits
8 bits
8 bits

## Slide 29: IP address class
1
Class A:
Bits:
0NNNNNNN
Host
Host
Host
8
9
16
17
24
25
32
Range (1-126)
1
Class B:
Bits:
10NNNNNN
Network
Host
Host
8
9
16
17
24
25
32
Range (128-191)
1
Class C:
Bits:
110NNNNN
Network
Network
Host
8
9
16
17
24
25
32
Range (192-223)
1
Class D:
Bits:
1110MMMM
Multicast Group
Multicast Group
Multicast Group
8
9
16
17
24
25
32
Range (224-239)

## Slide 30: Network & broadcast address
Network address
  All host bits are ‘0’
  Used by router
Broadcast address
  All host bits are ‘1’
  Send to all host in the network
Host address
  Others
  Assigned to a host

## Slide 31: Host address
172.16.2.2
172.16.3.10
172.16.12.12
10.1.1.1
10.250.8.11
10.180.30.118
E1
172.16
12
12
Network
Host
.
.
Network
Interface
172.16.0.0
10.0.0.0
E0
E1
Routing Table
172.16.2.1
10.6.24.2
E0

## Slide 32: Determining Available Host Addresses
11111111
172 16 0 0
10101100
00010000
00000000
00000000
16 15 14 13 12 11 10 9
8 7 6 5 4 3 2 1
Network
Host
00000000
00000001
11111111
11111111
11111111
11111110
...
...
00000000
00000011
11111101
1
2
3
65534
65535
65536
-
...
2
65534
N
2N-2 = 216-2 = 65534

## Slide 33: Subnet mask
172
16
0
0
255
255
0
0
255
255
255
0
IP Address
Default Subnet Mask
8-bit Subnet Mask
Network
Host
Network
Host
Network
Subnet
Host
Also written as “/16” where 16 represents the number of 1s in the mask.
Also written as “/24” where 24 represents the number of 1s in the mask.
11111111
11111111
00000000
00000000

## Slide 34: Decimal Equivalents of Bit Patterns
0 0 0 0 0 0 0 0 = 0
1 0 0 0 0 0 0 0 = 128
1 1 0 0 0 0 0 0 = 192
1 1 1 0 0 0 0 0 = 224
1 1 1 1 0 0 0 0 = 240
1 1 1 1 1 0 0 0 = 248
1 1 1 1 1 1 0 0 = 252
1 1 1 1 1 1 1 0 = 254
1 1 1 1 1 1 1 1 = 255
128 64 32 16 8 4 2 1

## Slide 35: Exercise
16
172
2
160
10101100
00010000
10100000
00000010
Host
Mask
Subnet
Broadcast
Last
First
172.16.2.160
255.255.255.192

## Slide 36: Private & public address

## Slide 37: Transport Layer Overview
Transmission Control
Protocol (TCP)
User Datagram
Protocol (UDP)
Application
Transport
Internet
Data Link
Physical
Connection-Oriented Connectionless
Notes: Tầng vận chuyển
Tầng vận chuyển là một mức ở dưới tầng ứng dụng và chức năng của nó là cung cấp dịch vụ để chuyển
dữ liệu giữa đầu cuối của hệ thống (end-to-end).
• TCP: Đảm bảo độ tin cậy cao.
• UDP: (Giao thức gói thông tin người dùng): Thay choviệc đảm bảo độ tin cậy cao, giao thức này đảm
bảo tốc độ cao.
Giao thức nào trong hai giao thức được sử dụng sẽ được xác định bởi tầng ứng dụng mức cao
hơn. TCP là phù hợp khi lượng dữ liệu lớn sẽ được truyền liên tục, và UDP là phù hợp khi dữ liệu kích
thước nhỏ (gói) được truyền không liên tục.

## Slide 38: TCP Segment Format
Source port (16)
Destination port (16)
Sequence number (32)
Header length (4)
Acknowledgement number (32)
Reserved (6)
Code bits (6)
Window (16)
Checksum (16)
Urgent (16)
Options (0 or 32 if any)
Data (varies)
20 Bytes
Bit 0
Bit 15
Bit 16
Bit 31
Notes: Purpose: This figure explains what is contained in a TCP segment.
Emphasize:
Source Port and Destination Port are the connections to the upper-layer protocol.
Sequence and Acknowledgment numbers are the position in the user’s byte stream of this segment. Sequence numbers are used for establishing reliability.
HLEN is the header length. It tells us where the data begins.
Six bits are reserved for future use.
Code Bits distinguish session management messages from data.
Window is a term we will come back to in a few slides. For now, consider it the size of the receivers buffers.
Checksum is a cyclic redundancy check (CRC). It verifies that the datagram arrived intact.
Urgent Pointer is used to signify out-of-band data.
Options are used by vendors to enhance their protocol offering.
The data portion of the frame contains the upper-layer protocol data.

## Slide 39: Port Numbers
TCP
Port Numbers
F T P
Transport Layer
T E L N E T
D N S
S N M P
T F T P
S M T P
UDP
Application Layer
21
23
25
53
69
161
R I P
520
Notes: Purpose: This figure explains how TCP uses port numbers to connect applications.
Emphasize: These port numbers were standardized in RFC 1340. This RFC has been obsoleted by RFC 1700. However, many of the port numbers outlined in RFC 1340 are still being used as standards.
It is possible to filter on TCP port numbers.
The TCP port number, combined with other information, is what UNIX C language developers call a socket. However, work sockets have different meanings in XNS and Novell, where they are service access point abstractions or programming interfaces rather than service access point identifiers.

## Slide 40: TCP Port Numbers
Source
Port
Dest.
Port
…
Host A
1028
23
…
SP
DP
Host Z
Telnet Z
Dest. port = 23. Send packet to my
Telnet application.
Notes: Purpose: This figure continues to explain how TCP uses port numbers.
Emphasize: In most cases the TCP port number on one side of a conversation is the same on the other side. For example, when a file transfer takes place, the software on one host is communicating with a peer application on another host.
In this example we see a Telnet (TCP port 23) session. It is possible to have multiple Telnet sessions running simultaneously on a host or router. Telnet selects an unused port number above 1023 to represent the source port for each independent session. Notice that the destination port is still 23.
Port numbering is important to understand in order to configure IP extended access lists. The lack of symmetry in port number use is a critical factor in establishing effective security.

## Slide 41: TCP Three Way Handshake/Open Connection
Send SYN
(seq=100 ctl=SYN)
SYN received
Host A
Host B
1
Notes: Layer 1 of 3:
Host A begins by sending a SYN segment indicating that host A will use sequence numbers starting with sequence number 100.
Emphasize: TCP is a simple protocol in terms of connection establishment. Some protocols have dozens of negotiation messages that are transmitted prior to session initialization.
TCP implements a strategy that is both necessary and sufficient.

## Slide 42: TCP Three Way Handshake/Open Connection
Send SYN
(seq=100 ctl=SYN)
SYN received
Send SYN, ACK
(seq=300 ack=101 ctl=syn,ack)
Host A
Host B
SYN received
1
2
Notes: Layer 2 of 3:
Host B sends an ACK and acknowledges the SYN it received from host A. Host B also sends a SYN. Note that the acknowledgment field indicates host B is now expecting to hear sequence 101, acknowledging the SYN that occupied sequence 100.

## Slide 43: TCP Three Way Handshake/Open Connection
Send SYN
(seq=100 ctl=SYN)
SYN received
Send SYN, ACK
(seq=300 ack=101 ctl=syn,ack)
Established
(seq=101 ack=301 ctl=ack)
Host A
Host B
1
2
3
SYN received
Notes: Layer 3 of 3:
In the next segment, host A sends some data. Note that the sequence number of the segment in step 3 is the same as as the ACK in step 2.
Emphasize: This sequence is like two people talking. The first person wants to talk to the second, so she says, “I would like to talk with you.” (SYN.) The second person responds, “Good. I want to talk with you.” (SYN, ACK.) The first person then says, “Fine—let us talk. Here is what I have to say.” (SYN, ACK, DATA.)
At this point either side can begin communicating and either side can break the connection. TCP is a peer-to-peer (balanced) communication method (no primary/secondary).
Note: This figure explains TCP connection establishment. For more information regarding the three-way handshake in establishing a TCP connection, refer to RFC 793.

## Slide 44: TCP Sequence and Acknowledgment Numbers
Source
Port
Dest.
Port
…
Sequence
#
Acknowledgement
#
Source
Dest.
Seq.
Ack.
1028
23
10
1
I just
sent #10.
Notes: Layer 1 of 4:
Layer 1 shows the Sequence number is 10.

## Slide 45: UDP Segment Format
No sequence or acknowledgment fields
Source port (16)
Destination port (16)
Length (16)
Data (if any)
1
Bit 0
Bit 15
Bit 16
Bit 31
Checksum (16)
8 Bytes
Notes: Purpose: This graphic explains the format of UDP.
Emphasize: UDP is simple and efficient but not reliable. The UDP segment format includes a source port, a destination port, a length field, and an optional checksum field. It has no sequencing, acknowledgments, or windowing.
Example: TFTP uses a checksum. At the end of the transfer if the checksum does not match then the file did not make it. The user is notified and must type in the command again. As a result, the user has become the reliability mechanism.
Transition: The next section discusses the network layer of the OSI model and how it corresponds to the TCP/IP internet layer.

## Slide 46: Mapping L2 Address to L3 Address
To send data to a destination, a host must know the physical (MAC) address of the destination
Address Resolution Protocol (ARP)
  Binding IP address – MAC address
  ARP request, ARP reply
  ARP table aging time
Notes: Địa chỉ MAC là gì?
Địa chỉ IP được sử dụng để phân biệt các nút kết nối tới một mạng. Tuy nhiên, việc nhận dạng địa chỉ IP
xẩy ra tại tầng giao thức TCP/IP. Vì vậy, địa chỉ có khả năng thực hiện nhận dạng ở tầng giao diện mạng
(một mức ở dưới tầng Internet) được yêu cầu để thựchiện truyền thông vật lý. Đó là địa chỉ MAC (Điều
khiển truy nhập phương tiện).
ARP (Giao thức phân giải địa chỉ)
Trong mô hình TCP/IP, địa chỉ IP được sử dụng như địa chỉ nơi nhận việc truyền. Tuy nhiên, trên thực tế để phát dữ liệu tới nơi nhận trong mạng, địa chỉ MAC của nơi nhận phải được xác định. Do đó cần phải ánh xạ địa chỉ IP tới địa chỉ MAC. ARP đóng vai trò của ánh xạ này.

## Slide 47: Mapping L2 Address to L3 Address

## Slide 48: Packet delivery

## Slide 49: IP Layer Operation

## Slide 50: ARP table lookup

## Slide 51: ARP request

## Slide 52: ARP learning

## Slide 53: ARP reply

## Slide 54: ARP update table

## Slide 55: Sending SYN packet

## Slide 56: Reply SYN ACK

## Slide 57: Send ACK

## Slide 58: Open session

## Slide 59: Data flow begins

## Slide 60: Data is ACKed